## Slide 1
EECS 20
Lecture 36 (April 23, 2001)
Tom Henzinger
Safety Control

## Slide 2
The Control Problem
Given
Plant
1.
2. Objective

## Slide 3
The Control Problem
Find
Plant
Controller
such that the composite (“closed-loop”) system satisfies the Objective

## Slide 4
Simple Control Problems
LTI Plant
Finite-State Plant

## Slide 5
Even Simple Linear Systems are Not Finite-State
x: Nats0  Reals
y: Nats0  Reals
 z  Nats0, y(z) =
0 if z=0
  (x(z-1) + x(z)) if z>0
{

## Slide 6
Even Simple Finite-State Systems are Not Linear
x: Nats0  Reals
y: Nats0  Reals
 z  Nats0, y(z) =
x(z) if  z’  z, x(z’)  100
0 if  z’  z, x(z’) > 100
{

## Slide 7
i  100 / i
i / 0
i > 100 / 0
( “i” stands for any input value )

## Slide 8
Simplest Finite-State Control Objective:
SAFETY
stay out of a set of undesirable plant states (the “error” states)

## Slide 9
The Finite-State Safety Control Problem
Given
finite-state machine Plant
1.
2. set Error of states of Plant

## Slide 10
The Finite-State Safety Control Problem
Find
finite-state machine Plant
finite-state machine Controller
such that the composite system never enters a state in Error

## Slide 11
Step 1:
Compute the “uncontrollable” states of Plant
Every state in Error is uncontrollable.
For all states s,
if for all inputs i there exist an uncontrollable state s’ and an output o such that (s’,o)  possibleUpdates (s,i)
then s is uncontrollable.

## Slide 12
i/0
i/0
Error
Plant
0/1
1/1
0/1
1/1
0/1
1/1
1/0
1/1
0/1
0/1
1/0
1/1
0/0

## Slide 13
i/0
i/0
Error
Plant
0/1
1/1
0/1
1/1
0/1
1/1
1/0
1/1
0/1
0/1
1/0
1/1
uncontrollable (cannot prevent error state from being entered in 1 transition)
0/0

## Slide 14
i/0
i/0
Error
Plant
0/1
1/1
0/1
1/1
0/1
1/1
1/0
1/1
0/1
0/1
1/0
1/1
uncontrollable (cannot prevent error state from being entered in 2 transitions)
0/0

## Slide 15
i/0
i/0
Error
Plant
0/1
1/1
0/1
1/1
0/1
1/1
1/0
1/1
0/1
0/1
1/0
1/1
Uncontrollable
0/0

## Slide 16
i/0
i/0
Error
Plant
0/1
1/1
0/1
1/1
0/1
1/1
1/0
1/1
0/1
0/1
1/0
1/1
Uncontrollable
safe control inputs
0/0

## Slide 17
Step 2:
Design the Controller
For each controllable state s of the plant, choose one input i so that possibleUpdates (s,i) contains only controllable states.

## Slide 18
r
q
p
i/0
i/0
Plant
0/1
1/1
0/1
1/1
0/1
1/1
1/0
1/1
0/1
0/1
1/0
1/1
Uncontrollable
chosen control inputs
p : 1 q : 1 r : 0
0/0

## Slide 19
Step 2:
Design the Controller
For each controllable state s of the plant, choose one input i so that possibleUpdates (s,i) contains only controllable states.
Have the Controller keep track of the state of the Plant:
If Plant is output-deterministic, then Controller looks exactly like the controllable part of Plant, with inputs and outputs swapped.

## Slide 20
Plant
r
q
p
i/0
i/0
0/1
1/1
0/1
1/1
0/1
1/1
1/0
1/1
0/1
0/1
1/0
1/1
Uncontrollable
Controller
r
q
p
0/1
1/0
0/1
1/1
1/1
0/0

## Slide 21
Plant
r
q
p
i/0
i/0
0/1
1/1
0/1
1/1
0/1
1/1
1/0
1/1
0/1
0/1
1/0
1/1
Uncontrollable
Controller
r
q
p
0/1
1/0
0/1
1/1
1/1
0/0
(the Controller can be made receptive in any way)
0/0

## Slide 22
What if the Plant is not output-deterministic?

## Slide 23
Plant
r
q
p
i/0
i/0
0/1
1/1
0/1
1/1
0/1
1/1
1/1
1/1
0/1
0/1
1/1
1/1
Uncontrollable
Controller
p,q
p
1/1
0/1

## Slide 24
Plant
r
q
p
i/0
i/0
0/1
1/1
0/1
1/1
0/1
1/1
1/1
1/1
0/1
0/1
1/1
1/1
Uncontrollable
Controller
p,q
p
1/1
p,q,r
1/1
0/1

## Slide 25
Plant
r
q
p
i/0
i/0
0/1
1/1
0/1
1/1
0/1
1/1
1/1
1/1
0/1
0/1
1/1
1/1
Uncontrollable
Controller
p,q
p
1/1
p,q,r
1/1
Neither 0 nor 1 is safe !
0/1

## Slide 26
Plant
r
q
p
i/0
i/0
0/1
1/1
0/1
1/1
0/1
1/1
1/1
1/1
0/1
0/1
1/1
1/1
Uncontrollable
0/1

## Slide 27
Plant
r
q
p
i/0
i/0
0/1
1/1
0/1
1/1
0/1
1/1
1/1
1/1
0/1
0/1
1/1
1/1
Uncontrollable
0/1
Controller
p,r
p
1/0

## Slide 28
Plant
r
q
p
i/0
i/0
0/1
1/1
0/1
1/1
0/1
1/1
1/1
1/1
0/1
0/1
1/1
1/1
Uncontrollable
0/1
Controller
p,r
p
1/0
1/0

## Slide 29
Step 2: Design the Controller
Let Controllable be the controllable states of the Plant. A subset S  Controllable is consistent if there is an input i such that for all states s  S, all states in possibleUpdates (s,i) are controllable.
Let M be the state machine whose states are the consistent subsets of Controllable. Prune from M the states that have no successor, until no more states can be pruned.
If the result contains possibleInitialStates (of the plant) as a state, then it is the desired Controller. Otherwise, no controller exists.

## Slide 30
Plant
r
q
p
i/0
i/0
0/1
1/1
0/1
1/1
0/1
1/1
1/1
1/1
0/1
0/1
1/1
1/1
Uncontrollable
0/1
Consistent subsets
{p} : 0, 1 {q} : 1 {r} : 0
{p,q} : 1 {p,r} : 0 {q,r}, {p,q,r} not consistent

## Slide 31
Plant
r
q
p
i/0
i/0
0/1
1/1
0/1
1/1
0/1
1/1
1/1
1/1
0/1
0/1
1/1
1/1
Uncontrollable
0/1
p
q
r
p,r
p,q
{p} : 0, 1 {q} : 1 {r} : 0 {p,q} : 1 {p,r} : 0

## Slide 32
Plant
r
q
p
i/0
i/0
0/1
1/1
0/1
1/1
0/1
1/1
1/1
1/1
0/1
0/1
1/1
1/1
Uncontrollable
0/1
p
q
r
p,r
p,q
{q} : 1 {r} : 0 {p,q} : 1 {p,r} : 0
1
0

## Slide 33
Plant
r
q
p
i/0
i/0
0/1
1/1
0/1
1/1
0/1
1/1
1/1
1/1
0/1
0/1
1/1
1/1
Uncontrollable
0/1
p
q
r
p,r
p,q
{r} : 0 {p,q} : 1 {p,r} : 0
1
0
1

## Slide 34
Plant
r
q
p
i/0
i/0
0/1
1/1
0/1
1/1
0/1
1/1
1/1
1/1
0/1
0/1
1/1
1/1
Uncontrollable
0/1
p
q
r
p,r
p,q
{p,q} : 1 {p,r} : 0
1
0
1
0

## Slide 35
Plant
r
q
p
i/0
i/0
0/1
1/1
0/1
1/1
0/1
1/1
1/1
1/1
0/1
0/1
1/1
1/1
Uncontrollable
0/1
p
q
r
p,r
{p,r} : 0
1
0
1
0
1
p,q

## Slide 36
Plant
r
q
p
i/0
i/0
0/1
1/1
0/1
1/1
0/1
1/1
1/1
1/1
0/1
0/1
1/1
1/1
Uncontrollable
0/1
p
q
r
p,r
1
0
1
0
p,q
0

## Slide 37
Plant
r
q
p
i/0
i/0
0/1
1/1
0/1
1/1
0/1
1/1
1/1
1/1
0/1
0/1
1/1
1/1
Uncontrollable
0/1
p
q
r
p,r
1
0
1
0
p,q
0

## Slide 38
Plant
r
q
p
i/0
i/0
0/1
1/1
0/1
1/1
0/1
1/1
1/1
1/1
0/1
0/1
1/1
1/1
Uncontrollable
0/1
p
q
r
p,r
0
1
0
0

## Slide 39
Plant
r
q
p
i/0
i/0
0/1
1/1
0/1
1/1
0/1
1/1
1/1
1/1
0/1
0/1
1/1
1/1
Uncontrollable
0/1
p
p,r
0
0

## Slide 40
Plant
r
q
p
i/0
i/0
0/1
1/1
0/1
1/1
0/1
1/1
1/1
1/1
0/1
0/1
1/1
1/1
Uncontrollable
0/1
Controller
p,r
p
i/0
i/0