## Slide 1: Finite State Machines
Sequential circuits
  primitive sequential elements
  combinational logic
Models for representing sequential circuits
  finite-state machines (Moore and Mealy)
Basic sequential circuits revisited
  shift registers
  counters
Design procedure
  state diagrams
  state transition table
  next state functions
Hardware description languages

## Slide 2: Abstraction of state elements
Divide circuit into combinational logic and state
Localize the feedback loops and make it easy to break cycles
Implementation of storage elements leads to various forms of sequential logic
Combinational Logic
Storage Elements
Outputs
State Outputs
State Inputs
Inputs

## Slide 3: Forms of sequential logic
Asynchronous sequential logic – state changes occur whenever state inputs change (elements may be simple wires or delay elements)
Synchronous sequential logic – state changes occur in lock step across all storage elements (using a periodic waveform - the clock)
Clock

## Slide 4: Finite state machine representations
In = 0
In = 1
In = 0
In = 1
100
010
110
111
001
States: determined by possible values in sequential storage elements
Transitions: change of state
Clock: controls when state can change by controlling storage elements
Sequential logic
  sequences through a series of states
  based on sequence of values on input signals
  clock period defines elements of sequence

## Slide 5: Example finite state machine diagram
Combination lock from introduction to course
  5 states
  5 self-transitions
  6 other transitions between states
  1 reset transition (from all states) to state S1
reset
S3
closed
closed
mux=C1
equal & new
not equal & new
not equal & new
not equal & new
not new
not new
not new
S1
S2
OPEN
ERR
closed
mux=C2
equal & new
closed
mux=C3
equal & new
open

## Slide 6: Can any sequential system be represented with a state diagram?
Shift register
  input value shown on transition arcs
  output values shown within state node
100
110
111
011
101
010
000
001
1
1
1
1
0
0
0
0
1
1
1
0
0
1
0
0
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
CLK

## Slide 7: Counters are simple finite state machines
010
100
110
011
001
000
101
111
3-bit up-counter
Counters
  proceed through well-defined sequence of states in response to enable
Many types of counters: binary, BCD, Gray-code
  3-bit up-counter: 000, 001, 010, 011, 100, 101, 110, 111, 000, ...
  3-bit down-counter: 111, 110, 101, 100, 011, 010, 001, 000, 111, ...

## Slide 8: How do we turn a state diagram into logic?
Counter
  3 flip-flops to hold state
  logic to compute next state
  clock signal controls when flip-flop memory can change
    wait long enough for combinational logic to compute new value
    don't wait too long as that is low performance
D
Q
D
Q
D
Q
OUT1
OUT2
OUT3
CLK
"1"

## Slide 9: FSM design procedure
Start with counters
  simple because output is just state
  simple because no choice of next state based on input
State diagram to state transition table
  tabular form of state diagram
  like a truth-table
State encoding
  decide on representation of states
  for counters it is simple: just its value
Implementation
  flip-flop for each state bit
  combinational logic based on encoding

## Slide 10: FSM design procedure: state diagram to encoded state transition table
010
100
110
011
001
000
101
111
3-bit up-counter
present state next state 0 000 001 1 1 001 010 2 2 010 011 3 3 011 100 4 4 100 101 5 5 101 110 6 6 110 111 7 7 111 000 0
Tabular form of state diagram
Like a truth-table (specify output for all input combinations)
Encoding of states: easy for counters – just use value

## Slide 11: Implementation
C3 C2 C1 N3 N2 N1 0 0 0 0 0 1 0 0 1 0 1 0 0 1 0 0 1 1 0 1 1 1 0 0 1 0 0 1 0 1 1 0 1 1 1 0 1 1 0 1 1 1 1 1 1 0 0 0
N1 <= C1’
N2 <= C1C2’ + C1’C2
<= C1 xor C2
N3 <= C1C2C3’ + C1’C3 + C2’C3
<= (C1C2)C3’ + (C1’ + C2’)C3
<= (C1C2)C3’ + (C1C2)’C3
<= (C1C2) xor C3
Verilog notation to show
function represents an input to D-FF
D flip-flop for each state bit
Combinational logic based on encoding
0 0
0 1
1 1
0 1
C1
C2
C3
N3
0 1
1 0
1 0
0 1
C1
C2
C3
N2
1 1
0 0
1 1
0 0
C1
C2
C3
N1

## Slide 12: Back to the shift register
In C1 C2 C3 N1 N2 N3 0 0 0 0 0 0 0 0 0 0 1 0 0 0 0 0 1 0 0 0 1 0 0 1 1 0 0 1 0 1 0 0 0 1 0 0 1 0 1 0 1 0 0 1 1 0 0 1 1 0 1 1 1 0 1 1 1 0 0 0 1 0 0 1 0 0 1 1 0 0 1 0 1 0 1 0 1 1 0 1 1 1 0 1 1 1 0 0 1 1 0 1 1 0 1 1 1 0 1 1 1 0 1 1 1 1 1 1 1 1 1 1
N1 <= In
N2 <= C1
N3 <= C2
Input determines next state
100
110
111
011
101
010
000
001
0
1
1
1
1
1
1
1
0
0
0
0
0
1
0
0
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
CLK

## Slide 13: More complex counter example
Complex counter
  repeats 5 states in sequence
  not a binary number representation
Step 1: derive the state transition diagram
  count sequence: 000, 010, 011, 101, 110
Step 2: derive the state transition table from the state transition diagram
Present State Next State
C B A C+ B+ A+
0 0 0 0 1 0
0 0 1 – – –
0 1 0 0 1 1
0 1 1 1 0 1
1 0 0 – – –
1 0 1 1 1 0
1 1 0 0 0 0
1 1 1 – – –
note the don't care conditions that arise from the unused state codes
010
000
110
101
011

## Slide 14: More complex counter example (cont’d)
C+ <= A
B+ <= B’ + A’C’
A+ <= BC’
Step 3: K-maps for next state functions
0 0
X 1
0 X
X 1
A
B
C
C+
1 1
X 0
0 X
X 1
A
B
C
B+
0 1
X 1
0 X
X 0
A
B
C
A+

## Slide 15: Self-starting counters (cont’d)
Re-deriving state transition table from don't care assignment
0 0
1 1
0 0
1 1
A
B
C
C+
1 1
1 0
0 1
0 1
A
B
C
B+
0 1
0 1
0 0
0 0
A
B
C
A+
Present State Next State
C B A C+ B+ A+
0 0 0 0 1 0
0 0 1 1 1 0
0 1 0 0 1 1
0 1 1 1 0 1
1 0 0 0 1 0
1 0 1 1 1 0
1 1 0 0 0 0
1 1 1 1 0 0
010
000
110
101
011
001
111
100

## Slide 16: Self-starting counters
Start-up states
  at power-up, counter may be in an unused or invalid state
  designer must guarantee that it (eventually) enters a valid state
Self-starting solution
  design counter so that invalid states eventually transition to a valid state
  may limit exploitation of don't cares
implementation
on previous slide
010
000
110
101
011
001
111
100
010
000
110
101
011
001
111
100

## Slide 17: Activity
2-bit up-down counter (2 inputs)
  direction: D = 0 for up, D = 1 for down
  count: C = 0 for hold, C = 1 for count
01
00
11
10
C=0 D=X
C=0 D=X
C=0 D=X
C=0 D=X
C=1 D=0
C=1 D=0
C=1 D=0
C=1 D=0
C=1 D=1
S1 S0 C D N1 N0 0 0 0 0 0 0 0 0 0 1 0 0 0 0 1 0 0 1 0 0 1 1 1 1 0 1 0 0 0 1 0 1 0 1 0 1 0 1 1 0 1 0 0 1 1 1 0 0 1 0 0 0 1 0 1 0 0 1 1 0 1 0 1 0 1 1 1 0 1 1 0 1 1 1 0 0 1 1 1 1 0 1 1 1 1 1 1 0 0 0 1 1 1 1 1 0

## Slide 18: Activity (cont’d)
S1 S0 C D N1 N0 0 0 0 0 0 0 0 0 0 1 0 0 0 0 1 0 0 1 0 0 1 1 1 1 0 1 0 0 0 1 0 1 0 1 0 1 0 1 1 0 1 0 0 1 1 1 0 0 1 0 0 0 1 0 1 0 0 1 1 0 1 0 1 0 1 1 1 0 1 1 0 1 1 1 0 0 1 1 1 1 0 1 1 1 1 1 1 0 0 0 1 1 1 1 1 0
N1 = C’S1
+ CDS0’S1’ + CDS0S1
+ CD’S0S1’ + CD’S0’S1
= C’S1
+ C(D’(S1  S0) + D(S1  S0))
N0 = CS0’ + C’S0
0 1 1 0
0 1 1 0 1 0 0 1
1 0 0 1
D
S1
S0
C
0 0 1 1
0 0 1 1 1 0 1 0
0 1 0 1
D
S1
S0
C

## Slide 19: Counter/shift-register model
Values stored in registers represent the state of the circuit
Combinational logic computes:
  next state
    function of current state and inputs
  outputs
    values of flip-flops
Inputs
Outputs
Next State
Current State
next state logic

## Slide 20: General state machine model
Values stored in registers represent the state of the circuit
Combinational logic computes:
  next state
    function of current state and inputs
  outputs
    function of current state and inputs (Mealy machine)
    function of current state only (Moore machine)
Inputs
Outputs
Next State
Current State
output logic
next state logic

## Slide 21: State machine model (cont’d)
States: S1, S2, ..., Sk
Inputs: I1, I2, ..., Im
Outputs: O1, O2, ..., On
Transition function: Fs(Si, Ij)
Output function: Fo(Si) or Fo(Si, Ij)
Inputs
Outputs
Next State
Current State
output logic
next state logic
Clock
Next State
State
0
1
2
3
4
5

## Slide 22: Comparison of Mealy and Moore machines
Mealy machines tend to have less states
  different outputs on arcs (n2) rather than states (n)
Moore machines are safer to use
  outputs change at clock edge (always one cycle later)
  in Mealy machines, input change can cause output change as soon as logic is done – a big problem when two machines are interconnected – asynchronous feedback may occur if one isn’t careful
Mealy machines react faster to inputs
  react in same cycle – don't need to wait for clock
  in Moore machines, more logic may be necessary to decode state into outputs – more gate delays after clock edge

## Slide 23: Comparison of Mealy and Moore machines (cont’d)
Moore
Mealy
Synchronous Mealy
state feedback
inputs
outputs
reg
combinational logic for next state
logic for outputs
inputs
outputs
state feedback
reg
combinational logic for next state
logic for outputs
inputs
outputs
state feedback
reg
combinational logic for next state
logic for outputs

## Slide 24: Specifying outputs for a Moore machine
D/1
E/1
B/0
A/0
C/0
1
0
0
0
0
1
1
1
1
0
reset
current next reset input state state output
1 – – A
0 0 A B 0
0 1 A C 0
0 0 B B 0
0 1 B D 0
0 0 C E 0
0 1 C C 0
0 0 D E 1
0 1 D C 1
0 0 E B 1
0 1 E D 1
Output is only function of state
  specify in state bubble in state diagram
  example: sequence detector for 01 or 10

## Slide 25: Specifying outputs for a Mealy machine
current next reset input state state output
1 – – A 0
0 0 A B 0
0 1 A C 0
0 0 B B 0
0 1 B C 1
0 0 C B 1
0 1 C C 0
B
A
C
0/1
0/0
0/0
1/1
1/0
1/0
reset/0
Output is function of state and inputs
  specify output on transition arc between states
  example: sequence detector for 01 or 10

## Slide 26: Registered Mealy machine (really Moore)
Synchronous (or registered) Mealy machine
  registered state AND outputs
  avoids ‘glitchy’ outputs
  easy to implement in PLDs
Moore machine with no output decoding
  outputs computed on transition to next state rather than after entering
  view outputs as expanded state vector
Inputs
Outputs
Current State
output logic
next state logic

## Slide 27: Example: vending machine
Vending Machine FSM
N
D
Reset
Clock
Open
Coin Sensor
Release Mechanism
Release item after 15 cents are deposited
Single coin slot for dimes, nickels
No change

## Slide 28: Example: vending machine (cont’d)
Suitable abstract representation
  tabulate typical input sequences:
    3 nickels
    nickel, dime
    dime, nickel
    two dimes
  draw state diagram:
    inputs: N, D, reset
    output: open chute
  assumptions:
    assume N and D asserted for one cycle
    each state has a self loop for N = D = 0 (no coin)
S0
Reset
S2
D
S6
[open]
D
S4
[open]
D
S1
N
S3
N
S5
[open]
N
S8
[open]
D
S7
[open]
N

## Slide 29: Example: vending machine (cont’d)
Minimize number of states - reuse states whenever possible
symbolic state table
present inputs next output state D N state open 0¢ 0 0 0¢ 0 0 1 5¢ 0 1 0 10¢ 0 1 1 – – 5¢ 0 0 5¢ 0 0 1 10¢ 0 1 0 15¢ 0 1 1 – – 10¢ 0 0 10¢ 0 0 1 15¢ 0 1 0 15¢ 0 1 1 – – 15¢ – – 15¢ 1
0¢
Reset
5¢
N
N
N + D
10¢
D
15¢
[open]
D

## Slide 30: Example: vending machine (cont’d)
present state inputs next state output Q1 Q0 D N D1 D0 open 0 0 0 0 0 0 0 0 1 0 1 0 1 0 1 0 0 1 1 – – – 0 1 0 0 0 1 0 0 1 1 0 0 1 0 1 1 0 1 1 – – – 1 0 0 0 1 0 0 0 1 1 1 0 1 0 1 1 0 1 1 – – – 1 1 – – 1 1 1
Uniquely encode states

## Slide 31: Example: Moore implementation
D1 = Q1 + D + Q0 N
D0 = Q0’ N + Q0 N’ + Q1 N + Q1 D
OPEN = Q1 Q0
Mapping to logic
0 0 1 1
0 1 1 1
X X 1 X
1 1 1 1
Q1
D1
Q0
N
D
0 1 1 0
1 0 1 1
X X 1 X
0 1 1 1
Q1
D0
Q0
N
D
0 0 1 0
0 0 1 0
X X 1 X
0 0 1 0
Q1
Open
Q0
N
D

## Slide 32: Example: vending machine (cont’d)
present state inputs next state output Q3 Q2 Q1 Q0 D N D3 D2 D1 D0 open 0 0 0 1 0 0 0 0 0 1 0 0 1 0 0 1 0 0 1 0 0 1 0 0 0 1 1 - - - - - 0 0 1 0 0 0 0 0 1 0 0 0 1 0 1 0 0 0 1 0 1 0 0 0 0 1 1 - - - - - 0 1 0 0 0 0 0 1 0 0 0 0 1 1 0 0 0 0 1 0 1 0 0 0 0 1 1 - - - - - 1 0 0 0 - - 1 0 0 0 1
D0 = Q0 D’ N’
D1 = Q0 N + Q1 D’ N’
D2 = Q0 D + Q1 N + Q2 D’ N’
D3 = Q1 D + Q2 D + Q2 N + Q3
OPEN = Q3
One-hot encoding

## Slide 33: Equivalent Mealy and Moore state diagrams
Moore machine
  outputs associated with state
0¢
[0]
10¢
[0]
5¢
[0]
15¢
[1]
N’ D’ + Reset
D
D
N
N+D
N
N’ D’
Reset’
N’ D’
N’ D’
Reset
0¢
10¢
5¢
15¢
(N’ D’ + Reset)/0
D/0
D/1
N/0
N+D/1
N/0
N’ D’/0
Reset’/1
N’ D’/0
N’ D’/0
Reset/0
Mealy machine
  outputs associated with transitions

## Slide 34: Example: Mealy implementation
0¢
10¢
5¢
15¢
Reset/0
D/0
D/1
N/0
N+D/1
N/0
N’ D’/0
Reset’/1
N’ D’/0
N’ D’/0
Reset/0
present state inputs next state output Q1 Q0 D N D1 D0 open 0 0 0 0 0 0 0 0 1 0 1 0 1 0 1 0 0 1 1 – – – 0 1 0 0 0 1 0 0 1 1 0 0 1 0 1 1 1 1 1 – – – 1 0 0 0 1 0 0 0 1 1 1 1 1 0 1 1 1 1 1 – – – 1 1 – – 1 1 1
D0 = Q0’N + Q0N’ + Q1N + Q1D
D1 = Q1 + D + Q0N
OPEN = Q1Q0 + Q1N + Q1D + Q0D
0 0 1 0
0 0 1 1
X X 1 X
0 1 1 1
Q1
Open
Q0
N
D

## Slide 35: Example: Mealy implementation
D0 = Q0’N + Q0N’ + Q1N + Q1D
D1 = Q1 + D + Q0N
OPEN = Q1Q0 + Q1N + Q1D + Q0D make sure OPEN is 0 when reset – by adding AND gate

## Slide 36: Vending machine: Moore to synch. Mealy
OPEN = Q1Q0 creates a combinational delay after Q1 and Q0 change in Moore implementation
This can be corrected by retiming, i.e., move flip-flops and logic through each other to improve delay
OPEN.d = (Q1 + D + Q0N)(Q0'N + Q0N' + Q1N + Q1D) = Q1Q0N' + Q1N + Q1D + Q0'ND + Q0N'D
Implementation now looks like a synchronous Mealy machine
  it is common for programmable devices to have FF at end of logic

## Slide 37: Vending machine: Mealy to synch. Mealy
OPEN.d = Q1Q0 + Q1N + Q1D + Q0D
OPEN.d = (Q1 + D + Q0N)(Q0'N + Q0N' + Q1N + Q1D) = Q1Q0N' + Q1N + Q1D + Q0'ND + Q0N'D
0 0 1 0
0 0 1 1
1 0 1 1
0 1 1 1
Q1
Open.d
Q0
N
D
0 0 1 0
0 0 1 1
X X 1 X
0 1 1 1
Q1
Open.d
Q0
N
D

## Slide 38: Mealy and Moore examples
Recognize A,B = 0,1
  Mealy or Moore?
B
A
out

## Slide 39: Mealy and Moore examples (cont’d)
Recognize A,B = 1,0 then 0,1
  Mealy or Moore?

## Slide 40: Hardware Description Languages and Sequential Logic
Flip-flops
  representation of clocks - timing of state changes
  asynchronous vs. synchronous
FSMs
  structural view (FFs separate from combinational logic)
  behavioral view (synthesis of sequencers – not in this course)
Data-paths = data computation (e.g., ALUs, comparators) + registers
  use of arithmetic/logical operators
  control of storage elements

## Slide 41: Example: reduce-1-string-by-1
Remove one 1 from every string of 1s on the input
1
0
0
0
1
1
zero [0]
one1 [0]
two1s
[1]
1/0
0/0
0/0
1/1
zero [0]
one1 [0]
Moore
Mealy

## Slide 42: Verilog FSM - Reduce 1s example
module reduce (clk, reset, in, out); input clk, reset, in; output out;
parameter zero = 2’b00; parameter one1 = 2’b01; parameter two1s = 2’b10; reg out; reg [2:1] state; // state variables reg [2:1] next_state; always @(posedge clk) if (reset) state = zero; else state = next_state;
state assignment (easy to change, if in one place)
Moore machine
1
0
0
0
1
1
zero [0]
one1 [0]
two1s
[1]

## Slide 43: Moore Verilog FSM (cont’d)
always @(in or state)
case (state) zero: // last input was a zero begin if (in) next_state = one1; else next_state = zero; end one1: // we've seen one 1 begin if (in) next_state = two1s; else next_state = zero; end two1s: // we've seen at least 2 ones begin if (in) next_state = two1s; else next_state = zero; end endcase
crucial to include all signals that are input to state determination
note that output depends only on state
always @(state) case (state) zero: out = 0; one1: out = 0; two1s: out = 1; endcase
endmodule

## Slide 44: Mealy Verilog FSM
module reduce (clk, reset, in, out); input clk, reset, in; output out; reg out; reg state; // state variables reg next_state; always @(posedge clk) if (reset) state = zero; else state = next_state; always @(in or state) case (state) zero: // last input was a zero begin out = 0; if (in) next_state = one; else next_state = zero; end one: // we've seen one 1 if (in) begin next_state = one; out = 1; end else begin next_state = zero; out = 0; end endcase endmodule
1/0
0/0
0/0
1/1
zero [0]
one1 [0]

## Slide 45: Synchronous Mealy Machine
module reduce (clk, reset, in, out); input clk, reset, in; output out; reg out; reg state; // state variables always @(posedge clk) if (reset) state = zero; else case (state) zero: // last input was a zero begin out = 0; if (in) state = one; else state = zero; end one: // we've seen one 1 if (in) begin state = one; out = 1; end else begin state = zero; out = 0; end endcase endmodule

## Slide 46: Finite state machines summary
Models for representing sequential circuits
  abstraction of sequential elements
  finite state machines and their state diagrams
  inputs/outputs
  Mealy, Moore, and synchronous Mealy machines
Finite state machine design procedure
  deriving state diagram
  deriving state transition table
  determining next state and output functions
  implementing combinational logic
Hardware description languages