## Slide 1: Why study logic design?
Obvious reasons
  this course is part of the CS/CompE requirements
  it is the implementation basis for all modern computing devices
    building large things from small components
    provide a model of how a computer works
More important reasons
  the inherent parallelism in hardware is often our first exposure to parallel computation
  it offers an interesting counterpoint to software design and is therefore useful in furthering our understanding of computation, in general

## Slide 2: What will we learn in this class?
The language of logic design
  Boolean algebra, logic minimization, state, timing, CAD tools
The concept of state in digital systems
  analogous to variables and program counters in software systems
How to specify/simulate/compile/realize our designs
  hardware description languages
  tools to simulate the workings of our designs
  logic compilers to synthesize the hardware blocks of our designs
  mapping onto programmable hardware
Contrast with software design
  sequential and parallel implementations
  specify algorithm as well as computing/storage resources it will use

## Slide 3: Applications of logic design
Conventional computer design
  CPUs, busses, peripherals
Networking and communications
  phones, modems, routers
Embedded products
  in cars, toys, appliances, entertainment devices
Scientific equipment
  testing, sensing, reporting
The world of computing is much much bigger than just PCs!

## Slide 4: A quick history lesson
1850: George Boole invents Boolean algebra
  maps logical propositions to symbols
  permits manipulation of logic statements using mathematics
1938: Claude Shannon links Boolean algebra to switches
  his Masters’ thesis
1945: John von Neumann develops the first stored program computer
  its switching elements are vacuum tubes (a big advance from relays)
1946: ENIAC . . . The world’s first completely electronic computer
  18,000 vacuum tubes
  several hundred multiplications per minute
1947: Shockley, Brittain, and Bardeen invent the transistor
  replaces vacuum tubes
  enable integration of multiple devices into one package
  gateway to modern electronics

## Slide 5: What is logic design?
What is design?
  given a specification of a problem, come up with a way of solving it choosing appropriately from a collection of available components
  while meeting some criteria for size, cost, power, beauty, elegance, etc.
What is logic design?
  determining the collection of digital logic components to perform a specified control and/or data manipulation and/or communication function and the interconnections between them
  which logic components to choose? – there are many implementation technologies (e.g., off-the-shelf fixed-function components, programmable devices, transistors on a chip, etc.)
  the design may need to be optimized and/or transformed to meet design constraints

## Slide 6: What is digital hardware?
sense
sense
drive
AND
Collection of devices that sense and/or control wires that carry a digital value (i.e., a physical quantity that can be interpreted as a “0” or “1”)
  example: digital logic where voltage < 0.8v is a “0” and > 2.0v is a “1”
  example: pair of transmission wires where a “0” or “1” is distinguished by which wire has a higher voltage (differential)
  example: orientation of magnetization signifies a “0” or a “1”
Primitive digital hardware devices
  logic computation devices (sense and drive)
    are two wires both “1” - make another be “1” (AND)
    is at least one of two wires “1” - make another be “1” (OR)
    is a wire “1” - then make another be “0” (NOT)
  memory devices (store)
    store a value
    recall a previously stored value

## Slide 7: What is happening now in digital design?
Important trends in how industry does hardware design
  larger and larger designs
  shorter and shorter time to market
  cheaper and cheaper products
Scale
  pervasive use of computer-aided design tools over hand methods
  multiple levels of design representation
Time
  emphasis on abstract design representations
  programmable rather than fixed function components
  automatic synthesis techniques
  importance of sound design methodologies
Cost
  higher levels of integration
  use of simulation to debug designs
  simulate and verify before you build

## Slide 8: CSE 370: concepts/skills/abilities
New ability: to accomplish the logic design task with the aid of computer-aided design tools and map a problem description into an implementation with programmable logic devices after validation via simulation and understanding of the advantages/disadvantages as compared to a software implementation
Understanding the basics of logic design (concepts)
Understanding sound design methodologies (concepts)
Modern specification methods (concepts)
Familiarity with a full set of CAD tools (skills)
Realize digital designs in an implementation technology (skills)
Appreciation for the differences and similarities (abilities) in hardware and software design

## Slide 9: Computation: abstract vs. implementation
Up to now, computation has been a mental exercise (paper, programs)
This class is about physically implementing computation using physical devices that use voltages to represent logical values
Basic units of computation are:
  representation: "0", "1" on a wire set of wires (e.g., for binary ints)
  assignment: x = y
  data operations: x + y – 5
  control: sequential statements: A; B; C conditionals: if x == 1 then y loops: for ( i = 1 ; i == 10, i++) procedures: A; proc(...); B;
We will study how each of these are implemented in hardware and composed into computational structures

## Slide 10: Switches: basic element of physical implementations
close switch (if A is “1” or asserted) and turn on light bulb (Z)
A
Z
open switch (if A is “0” or unasserted) and turn off light bulb (Z)
Implementing a simple circuit (arrow shows action if wire changes to “1”):
Z  A
A
Z

## Slide 11: Switches (cont’d)
AND
OR
Z  A and B
Z  A or B
A
B
A
B
Compose switches into more complex ones (Boolean functions):

## Slide 12: Switching networks
Switch settings
  determine whether or not a conducting path exists to light the light bulb
To build larger computations
  use a light bulb (output of the network) to set other switches (inputs to another network).
Connect together switching networks
  to construct larger switching networks, i.e., there is a way to connect outputs of one network to the inputs of the next.

## Slide 13: Relay networks
conducting path composed of switches closes circuit
current flowing through coil magnetizes core and causes normally closed (nc) contact to be pulled open
when no current flows, the spring of the contact returns it to its normal position
A simple way to convert between conducting paths and switch settings is to use (electro-mechanical) relays.
What is a relay? What determines the switching speed of a relay network?

## Slide 14: Transistor networks
Relays aren't used much anymore
  some traffic light controllers are still electro-mechanical
Modern digital systems are designed in CMOS technology
  MOS stands for Metal-Oxide on Semiconductor
  C is for complementary because there are both normally-open and normally-closed switches
MOS transistors act as voltage-controlled switches
  similar, though easier to work with than relays.

## Slide 15: MOS transistors
n-channel open when voltage at G is low closes when:
voltage(G) > voltage (S) + 
p-channel closed when voltage at G is low opens when:
voltage(G) < voltage (S) – 
MOS transistors have three terminals: drain, gate, and source
  they act as switches in the following way: if the voltage on the gate terminal is (some amount) higher/lower than the source terminal then a conducting path will be established between the drain and source terminals
G
S
D
G
S
D

## Slide 16: MOS networks
3v
X
Y
0 volts
x
y
3 volts
0v
what is the relationship between x and y?
0 volts
3 volts

## Slide 17: Two input networks
x
y
z1 z2
0 volts
3 volts
0 volts
3 volts
0 volts
0 volts
3 volts
3 volts
what is the relationship between x, y and z?
3v
X
Y
0v
Z1
3v
X
Y
0v
Z2
3 volts
3 volts
3 volts
0 volts
3 volts
0 volts
0 volts
0 volts
NAND
NOR

## Slide 18: Speed of MOS networks
What influences the speed of CMOS networks?
  charging and discharging of voltages on wires and gates of transistors
Capacitors hold charge
  capacitance is at gates of transistors and wire material
Resistors slow movement of electrons
  resistance mostly due to transistors

## Slide 19: Representation of digital designs
scope of CSE 370
Physical devices (transistors, relays)
Switches
Truth tables
Boolean algebra
Gates
Waveforms
Finite state behavior
Register-transfer behavior
Concurrent abstract specifications

## Slide 20: Digital vs. analog
Convenient to think of digital systems as having only discrete, digital, input/output values
In reality, real electronic components exhibit continuous, analog, behavior
Why do we make the digital abstraction anyway?
  switches operate this way
  easier to think about a small number of discrete values
Why does it work?
  does not propagate small errors in values
  always resets to 0 or 1

## Slide 21: Mapping from physical world to binary world
Technology State 0 State 1
Relay logic Circuit Open Circuit Closed CMOS logic 0.0-1.0 volts 2.0-3.0 volts Transistor transistor logic (TTL) 0.0-0.8 volts 2.0-5.0 volts Fiber Optics Light off Light on
Dynamic RAM Discharged capacitor Charged capacitor
Nonvolatile memory (erasable) Trapped electrons No trapped electrons
Programmable ROM Fuse blown Fuse intact
Bubble memory No magnetic bubble Bubble present
Magnetic disk No flux reversal Flux reversal
Compact disc No pit Pit

## Slide 22: Combinational vs. sequential digital circuits
inputs
outputs
system
A simple model of a digital system is a unit with inputs and outputs:
Combinational means "memory-less"
  a digital circuit is combinational if its output values only depend on its input values

## Slide 23: Combinational logic symbols
easy to implement with CMOS transistors (the switches we have available and use most)
Common combinational logic systems have standard symbols called logic gates
  Buffer, NOT
  AND, NAND
  OR, NOR
Z
A
B
Z
Z
A
A
B

## Slide 24: Sequential logic
Sequential systems
  exhibit behaviors (output values) that depend not only on the current input values, but also on previous input values
In reality, all real circuits are sequential
  because the outputs do not change instantaneously after an input change
  why not, and why is it then sequential?
A fundamental abstraction of digital design is to reason (mostly) about steady-state behaviors
  look at the outputs only after sufficient time has elapsed for the system to make its required changes and settle down

## Slide 25: Synchronous sequential digital systems
Outputs of a combinational circuit depend only on current inputs
  after sufficient time has elapsed
Sequential circuits have memory
  even after waiting for the transient activity to finish
The steady-state abstraction is so useful that most designers use a form of it when constructing sequential circuits:
  the memory of a system is represented as its state
  changes in system state are only allowed to occur at specific times controlled by an external periodic clock
  the clock period is the time that elapses between state changes it must be sufficiently long so that the system reaches a steady-state before the next state change at the end of the period

## Slide 26: Example of combinational and sequential logic
B
A
C
Clock
Combinational:
  input A, B
  wait for clock edge
  observe C
  wait for another clock edge
  observe C again: will stay the same
Sequential:
  input A, B
  wait for clock edge
  observe C
  wait for another clock edge
  observe C again: may be different

## Slide 27: Abstractions
Some we've seen already
  digital interpretation of analog values
  transistors as switches
  switches as logic gates
  use of a clock to realize a synchronous sequential circuit
Some others we will see
  truth tables and Boolean algebra to represent combinational logic
  encoding of signals with more than two logical values into binary form
  state diagrams to represent sequential logic
  hardware description languages to represent digital logic
  waveforms to represent temporal behavior

## Slide 28: An example
Calendar subsystem: number of days in a month (to control watch display)
  used in controlling the display of a wrist-watch LCD screen
  inputs: month, leap year flag
  outputs: number of days

## Slide 29: Implementation in software
integer number_of_days ( month, leap_year_flag) {
  switch (month) {
    case 1: return (31);
    case 2: if (leap_year_flag == 1) then return (29) else return (28);
    case 3: return (31);
    ...
    case 12: return (31);
    default: return (0);
  }
}

## Slide 30: Implementation as a combinational digital system
leap
month
d28
d29
d30
d31
month leap d28 d29 d30 d31 0000 – – – – – 0001 – 0 0 0 1 0010 0 1 0 0 0 0010 1 0 1 0 0 0011 – 0 0 0 1 0100 – 0 0 1 0 0101 – 0 0 0 1 0110 – 0 0 1 0 0111 – 0 0 0 1 1000 – 0 0 0 1 1001 – 0 0 1 0 1010 – 0 0 0 1 1011 – 0 0 1 0 1100 – 0 0 0 1 1101 – – – – – 111– – – – – –
Encoding:
  how many bits for each input/output?
  binary number for month
  four wires for 28, 29, 30, and 31
Behavior:
  combinational
  truth table specification

## Slide 31: Combinational example (cont’d)
symbol for and
symbol for or
symbol for not
Truth-table to logic to switches to gates
  d28 = 1 when month=0010 and leap=0
  d28 = m8'•m4'•m2•m1'•leap'
  d31 = 1 when month=0001 or month=0011 or ... month=1100
  d31 = (m8'•m4'•m2'•m1) + (m8'•m4'•m2•m1) + ... (m8•m4•m2'•m1')
  d31 = can we simplify more?
month leap d28 d29 d30 d31 0001 – 0 0 0 1 0010 0 1 0 0 0 0010 1 0 1 0 0 0011 – 0 0 0 1 0100 – 0 0 1 0 ... 1100 – 0 0 0 1 1101 – – – – – 111– – – – – – 0000 – – – – –

## Slide 32: Combinational example (cont’d)
d28 = m8'•m4'•m2•m1'•leap’
d29 = m8'•m4'•m2•m1'•leap
d30 = (m8'•m4•m2'•m1') + (m8'•m4•m2•m1') + (m8•m4'•m2'•m1) + (m8•m4'•m2•m1) = (m8'•m4•m1') + (m8•m4'•m1)
d31 = (m8'•m4'•m2'•m1) + (m8'•m4'•m2•m1) + (m8'•m4•m2'•m1) + (m8'•m4•m2•m1) + (m8•m4'•m2'•m1') + (m8•m4'•m2•m1') + (m8•m4•m2'•m1')

## Slide 33: Activity
How much can we simplify d31?
What if we started the months with 0 instead of 1? (i.e., January is 0000 and December is 1011)
d31 is true if: month is 7 or less and odd (1, 3, 5, 7), or month is 8 or more and even (8, 10, 12, and includes 14)
d31 is true if: m8 is 0 and m1 is 1, or m8 is 1 and m1 is 0 d31 = m8’m1 + m8m1’
More complex expression (0, 2, 4, 6, 7, 9, 11):
d31 = m8’m4’m2’m1’ + m8’m4’m2m1’ + m8’m4m2’m1’ + m8’m4m2m1’ + m8’m4m2m1 + m8m4’m2’m1 + m8m4’m2m1
d31 = m8’m1’ + m8’m4m2 + m8m1 (includes 13 and 15)
d31 = (d28 + d29 + d30)’

## Slide 34: Combinational example (cont’d)
d28 = m8'•m4'•m2•m1'•leap’
d29 = m8'•m4'•m2•m1'•leap
d30 = (m8'•m4•m2'•m1') + (m8'•m4•m2•m1') + (m8•m4'•m2'•m1) + (m8•m4'•m2•m1)
d31 = (m8'•m4'•m2'•m1) + (m8'•m4'•m2•m1) + (m8'•m4•m2'•m1) + (m8'•m4•m2•m1) + (m8•m4'•m2'•m4') + (m8•m4'•m2•m1') + (m8•m4•m2'•m1')

## Slide 35: Another example
Door combination lock:
  punch in 3 values in sequence and the door opens; if there is an error the lock must be reset; once the door opens the lock must be reset
  inputs: sequence of input values, reset
  outputs: door open/close
  memory: must remember combination or always have it available as an input

## Slide 36: Implementation in software
integer combination_lock ( ) {
  integer v1, v2, v3;
  integer error = 0;
  static integer c[3] = 3, 4, 2;
  while (!new_value( ));
  v1 = read_value( );
  if (v1 != c[1]) then error = 1;
  while (!new_value( ));
  v2 = read_value( );
  if (v2 != c[2]) then error = 1;
  while (!new_value( ));
  v3 = read_value( );
  if (v2 != c[3]) then error = 1;
  if (error == 1) then return(0); else return (1);
}

## Slide 37: Implementation as a sequential digital system
Encoding:
  how many bits per input value?
  how many values in sequence?
  how do we know a new input value is entered?
  how do we represent the states of the system?
Behavior:
  clock wire tells us when it’s ok to look at inputs (i.e., they have settled after change)
  sequential: sequence of values must be entered
  sequential: remember if an error occurred
  finite-state specification
reset
value
open/closed
new
clock
state

## Slide 38: Sequential example (cont’d): abstract control
C2!=value & new
C3!=value & new
reset
not new
not new
not new
closed
S1
closed
C1=value & new
S2
closed
C2=value & new
S3
C3=value & new
OPEN
open
C1!=value & new
closed
ERR
Finite-state diagram
  states: 5 states
    represent point in execution of machine
    each state has outputs
  transitions: 6 from state to state, 5 self transitions, 1 global
    changes of state occur when clock says it’s ok
    based on value of inputs
  inputs: reset, new, results of comparisons
  output: open/closed

## Slide 39: Sequential example (cont’d): data-path vs. control
reset
open/closed
new
C1
C2
C3
comparator
value
equal
multiplexer
equal
controller
mux control
clock
Internal structure
  data-path
    storage for combination
    comparators
  control
    finite-state machine controller
    control for data-path
    state changes controlled by clock

## Slide 40: Sequential example (cont’d): finite-state machine
closed
closed
mux=C1
reset
equal & new
not equal & new
not equal & new
not equal & new
not new
not new
not new
S1
S2
S3
OPEN
ERR
closed
mux=C2
equal & new
closed
mux=C3
equal & new
open
Finite-state machine
  refine state diagram to include internal structure

## Slide 41: Sequential example (cont’d): finite-state machine
reset new equal state state mux open/closed 1 – – – S1 C1 closed 0 0 – S1 S1 C1 closed 0 1 0 S1 ERR – closed 0 1 1 S1 S2 C2 closed 0 0 – S2 S2 C2 closed 0 1 0 S2 ERR – closed 0 1 1 S2 S3 C3 closed 0 0 – S3 S3 C3 closed 0 1 0 S3 ERR – closed 0 1 1 S3 OPEN – open 0 – – OPEN OPEN – open 0 – – ERR ERR – closed
next
Finite-state machine
  generate state table (much like a truth-table)
closed
closed
mux=C1
reset
equal & new
not equal & new
not equal & new
not equal & new
not new
not new
not new
S1
S2
S3
OPEN
ERR
closed
mux=C2
equal & new
closed
mux=C3
equal & new
open

## Slide 42: Sequential example (cont’d): encoding
Encode state table
  state can be: S1, S2, S3, OPEN, or ERR
    needs at least 3 bits to encode: 000, 001, 010, 011, 100
    and as many as 5: 00001, 00010, 00100, 01000, 10000
    choose 4 bits: 0001, 0010, 0100, 1000, 0000
  output mux can be: C1, C2, or C3
    needs 2 to 3 bits to encode
    choose 3 bits: 001, 010, 100
  output open/closed can be: open or closed
    needs 1 or 2 bits to encode
    choose 1 bits: 1, 0

## Slide 43: Sequential example (cont’d): encoding
good choice of encoding!
mux is identical to last 3 bits of state open/closed is identical to first bit of state
Encode state table
  state can be: S1, S2, S3, OPEN, or ERR
    choose 4 bits: 0001, 0010, 0100, 1000, 0000
  output mux can be: C1, C2, or C3
    choose 3 bits: 001, 010, 100
  output open/closed can be: open or closed
    choose 1 bits: 1, 0
reset new equal state state mux open/closed 1 – – – 0001 001 0 0 0 – 0001 0001 001 0 0 1 0 0001 0000 – 0 0 1 1 0001 0010 010 0 0 0 – 0010 0010 010 0 0 1 0 0010 0000 – 0 0 1 1 0010 0100 100 0 0 0 – 0100 0100 100 0 0 1 0 0100 0000 – 0 0 1 1 0100 1000 – 1 0 – – 1000 1000 – 1 0 – – 0000 0000 – 0
next

## Slide 44: Activity
Have lock always wait for 3 key presses exactly before making a decision
  remove reset
not equal & new
not equal & new
closed
mux=C1
equal & new
not new
not new
not new
S1
S2
S3
OPEN
closed
mux=C2
equal & new
closed
mux=C3
equal & new
open
not equal & new
closed
E2
not new
not new
closed
E3
new
closed
ERR
new

## Slide 45: Sequential example (cont’d): controller implementation
reset
open/closed
new
equal
controller
mux control
clock
reset
open/closed
new
equal
mux control
clock
comb. logic
state
special circuit element, called a register, for remembering inputs
when told to by clock
Implementation of the controller

## Slide 46: Design hierarchy
system
data-path
control
state registers
combinational logic
multiplexer
comparator
code registers
register
logic
switching networks

## Slide 47: Summary
That was what the entire course is about
  converting solutions to problems into combinational and sequential networks effectively organizing the design hierarchically
  doing so with a modern set of design tools that lets us handle large designs effectively
  taking advantage of optimization opportunities
Now lets do it again
  this time we'll take nine weeks instead of one