## Slide 1: Working with combinational logic
Simplification
  two-level simplification
  exploiting don’t cares
  algorithm for simplification
Logic realization
  two-level logic and canonical forms realized with NANDs and NORs
  multi-level logic, converting between ANDs and ORs
Time behavior
Hardware description languages

## Slide 2: Design example: two-bit comparator
we'll need a 4-variable Karnaugh map for each of the 3 output functions
block diagram
LT EQ GT
A B < C D A B = C D A B > C D
A
B
C
D
N1
N2
A B C D LT EQ GT
0 0 0 0 0 1 0
0 1 1 0 0
1 0 1 0 0
1 1 1 0 0
0 1 0 0 0 0 1
0 1 0 1 0
1 0 1 0 0
1 1 1 0 0
1 0 0 0 0 0 1
0 1 0 0 1
1 0 0 1 0
1 1 1 0 0
1 1 0 0 0 0 1
0 1 0 0 1
1 0 0 0 1
1 1 0 1 0
and
truth table

## Slide 3: Design example: two-bit comparator (cont’d)
A' B' D + A' C + B' C D
B C' D' + A C' + A B D'
LT =
EQ =
GT =
K-map for EQ
K-map for LT
K-map for GT
0 0
1 0
0 0
0 0
D
A
1 1
1 1
0 1
0 0
B
C
1 0
0 1
0 0
0 0
D
A
0 0
0 0
1 0
0 1
B
C
0 1
0 0
1 1
1 1
D
A
0 0
0 0
0 0
1 0
B
C
= (A xnor C) • (B xnor D)
LT and GT are similar (flip A/C and B/D)
A' B' C' D' + A' B C' D + A B C D + A B' C D’

## Slide 4: Design example: two-bit comparator (cont’d)
two alternative
implementations of EQ
with and without XOR
XNOR is implemented with at least 3 simple gates
A B C D
EQ
EQ

## Slide 5: Design example: 2x2-bit multiplier
block diagram
and
truth table
4-variable K-map
for each of the 4
output functions
A2 A1 B2 B1 P8 P4 P2 P1
0 0 0 0 0 0 0 0
0 1 0 0 0 0
1 0 0 0 0 0
1 1 0 0 0 0
0 1 0 0 0 0 0 0
0 1 0 0 0 1
1 0 0 0 1 0
1 1 0 0 1 1
1 0 0 0 0 0 0 0
0 1 0 0 1 0
1 0 0 1 0 0
1 1 0 1 1 0
1 1 0 0 0 0 0 0
0 1 0 0 1 1 1 0 0 1 1 0
1 1 1 0 0 1
P1
P2 P4
P8
A1
A2 B1
B2

## Slide 6: Design example: 2x2-bit multiplier (cont’d)
K-map for P8
K-map for P4
K-map for P2
K-map for P1
0 0
0 0
0 0
0 0
B1
A2
0 0
0 0
0 1
1 1
A1
B2
0 0
0 1
0 0
1 0
B1
A2
0 1
0 0
1 0
0 0
A1
B2
0 0
0 0
0 0
1 1
B1
A2
0 1
0 1
0 1
1 0
A1
B2
0 0
0 0
0 0
0 0
B1
A2
0 0
0 0
1 0
0 0
A1
B2
P8 = A2A1B2B1
P4 = A2B2B1' + A2A1'B2
P2 = A2'A1B2 + A1B2B1' + A2B2'B1 + A2A1'B1
P1 = A1B1

## Slide 7: Design example: BCD increment by 1
I8 I4 I2 I1 O8 O4 O2 O1 0 0 0 0 0 0 0 1
0 0 0 1 0 0 1 0
0 0 1 0 0 0 1 1
0 0 1 1 0 1 0 0
0 1 0 0 0 1 0 1
0 1 0 1 0 1 1 0
0 1 1 0 0 1 1 1
0 1 1 1 1 0 0 0
1 0 0 0 1 0 0 1
1 0 0 1 0 0 0 0
1 0 1 0 X X X X
1 0 1 1 X X X X
1 1 0 0 X X X X
1 1 0 1 X X X X
1 1 1 0 X X X X
1 1 1 1 X X X X
block diagram
and
truth table
4-variable K-map for each of the 4 output functions
O1
O2 O4
O8
I1
I2 I4
I8

## Slide 8: Design example: BCD increment by 1 (cont’d)
O8 = I4 I2 I1 + I8 I1'
O4 = I4 I2' + I4 I1' + I4’ I2 I1 O2 = I8’ I2’ I1 + I2 I1'
O1 = I1'
O8
O4
O2
O1
0 0
0 0
X 1
X 0
I1
I8
0 1
0 0
X X
X X
I4
I2
0 0
1 1
X 0
X 0
I1
I8
0 0
1 1
X X
X X
I4
I2
0 1
0 1
X 0
X 0
I1
I8
1 0
0 1
X X
X X
I4
I2
1 1
0 0
X 1
X 0
I1
I8
0 0
1 1
X X
X X
I4
I2

## Slide 9: Definition of terms for two-level simplification
Implicant
  single element of ON-set or DC-set or any group of these elements that can be combined to form a subcube
Prime implicant
  implicant that can't be combined with another to form a larger subcube
Essential prime implicant
  prime implicant is essential if it alone covers an element of ON-set
  will participate in ALL possible covers of the ON-set
  DC-set used to form prime implicants but not to make implicant essential
Objective:
  grow implicant into prime implicants (minimize literals per term)
  cover the ON-set with as few prime implicants as possible (minimize number of product terms)

## Slide 10: Examples to illustrate terms
0 X
1 1
1 0
1 0
D
A
1 0
0 0
1 1
1 1
B
C
5 prime implicants: BD, ABC', ACD, A'BC, A'C'D
0 0
1 1
1 0
1 0
D
A
0 1
0 1
1 1
0 0
B
C
6 prime implicants: A'B'D, BC', AC, A'C'D, AB, B'CD
minimum cover: AC + BC' + A'B'D
essential
minimum cover: 4 essential implicants
essential

## Slide 11: Algorithm for two-level simplification
Algorithm: minimum sum-of-products expression from a Karnaugh map
  Step 1: choose an element of the ON-set
  Step 2: find "maximal" groupings of 1s and Xs adjacent to that element
    consider top/bottom row, left/right column, and corner adjacencies
    this forms prime implicants (number of elements always a power of 2)
  Repeat Steps 1 and 2 to find all prime implicants
  Step 3: revisit the 1s in the K-map
    if covered by single prime implicant, it is essential, and participates in final cover
    1s covered by essential prime implicant do not need to be revisited
  Step 4: if there remain 1s not covered by essential prime implicants
    select the smallest number of prime implicants that cover the remaining 1s

## Slide 12: Algorithm for two-level simplification (example)
X 1
0 1
0 1
1 1
D
A
0 X
0 1
X 0
0 1
B
C
3 primes around AB'C'D'
X 1
0 1
0 1
1 1
D
A
0 X
0 1
X 0
0 1
B
C
2 primes around A'BC'D'
X 1
0 1
0 1
1 1
D
A
0 X
0 1
X 0
0 1
B
C
2 primes around ABC'D
X 1
0 1
0 1
1 1
D
A
0 X
0 1
X 0
0 1
B
C
minimum cover (3 primes)
X 1
0 1
0 1
1 1
D
A
0 X
0 1
X 0
0 1
B
C
X 1
0 1
0 1
1 1
D
A
0 X
0 1
X 0
0 1
B
C
2 essential primes
X 1
0 1
0 1
1 1
D
A
0 X
0 1
X 0
0 1
B
C

## Slide 13: Activity
X 0
0 1
X 0
X 1
D
A
0 X
X 1
X 0
1 1
B
C
BC
BD
AB
AC’D
CD’
BD
CD’
AC’D
BD
CD’
AC’D
List all prime implicants for the following K-map:
Which are essential prime implicants?
What is the minimum cover?
X 0
0 1
X 0
X 1
D
A
0 X
X 1
X 0
1 1
B
C

## Slide 14: Implementations of two-level logic
Sum-of-products
  AND gates to form product terms (minterms)
  OR gate to form sum
Product-of-sums
  OR gates to form sum terms (maxterms)
  AND gates to form product

## Slide 15: Two-level logic using NAND gates
Replace minterm AND gates with NAND gates
Place compensating inversion at inputs of OR gate

## Slide 16: Two-level logic using NAND gates (cont’d)
OR gate with inverted inputs is a NAND gate
  de Morgan’s: A’ + B’ = (A • B)’
Two-level NAND-NAND network
  inverted inputs are not counted
  in a typical circuit, inversion is done once and signal distributed

## Slide 17: Two-level logic using NOR gates
Replace maxterm OR gates with NOR gates
Place compensating inversion at inputs of AND gate

## Slide 18: Two-level logic using NOR gates (cont’d)
AND gate with inverted inputs is a NOR gate
  de Morgan’s: A’ • B’ = (A + B)’
Two-level NOR-NOR network
  inverted inputs are not counted
  in a typical circuit, inversion is done once and signal distributed

## Slide 19: Two-level logic using NAND and NOR gates
NAND-NAND and NOR-NOR networks
  de Morgan’s law: (A + B)’ = A’ • B’ (A • B)’ = A’ + B’
  written differently: A + B = (A’ • B’)’ (A • B) = (A’ + B’)’
In other words ––
  OR is the same as NAND with complemented inputs
  AND is the same as NOR with complemented inputs
  NAND is the same as OR with complemented inputs
  NOR is the same as AND with complemented inputs

## Slide 20: Conversion between forms
A
B
C
D
Z
A
B
C
D
Z
NAND
NAND
NAND
Convert from networks of ANDs and ORs to networks of NANDs and NORs
  introduce appropriate inversions ("bubbles")
Each introduced "bubble" must be matched by a corresponding "bubble"
  conservation of inversions
  do not alter logic function
Example: AND/OR to NAND/NAND

## Slide 21: Conversion between forms (cont’d)
Z = [ (A • B)’ • (C • D)’ ]’
= [ (A’ + B’) • (C’ + D’) ]’
= [ (A’ + B’)’ + (C’ + D’)’ ]
= (A • B) + (C • D) 
Example: verify equivalence of two forms
A
B
C
D
Z
A
B
C
D
Z
NAND
NAND
NAND

## Slide 22: Conversion between forms (cont’d)
Step 2
conserve
"bubbles"
Step 1
conserve
"bubbles"
NOR
NOR
NOR
\A
\B
\C
\D
Z
NOR
NOR
A
B
C
D
Z
Example: map AND/OR network to NOR/NOR network
A
B
C
D
Z

## Slide 23: Conversion between forms (cont’d)
Z = { [ (A’ + B’)’ + (C’ + D’)’ ]’ }’
= { (A’ + B’) • (C’ + D’) }’
= (A’ + B’)’ + (C’ + D’)’
= (A • B) + (C • D) 
Example: verify equivalence of two forms
A
B
C
D
Z
NOR
NOR
NOR
\A
\B
\C
\D
Z

## Slide 24: Multi-level logic
A
B C
D E F G
X
x = A D F + A E F + B D F + B E F + C D F + C E F + G
  reduced sum-of-products form – already simplified
  6 x 3-input AND gates + 1 x 7-input OR gate (that may not even exist!)
  25 wires (19 literals plus 6 internal wires)
x = (A + B + C) (D + E) F + G
  factored form – not written as two-level S-o-P
  1 x 3-input OR gate, 2 x 2-input OR gates, 1 x 3-input AND gate
  10 wires (7 literals plus 3 internal wires)

## Slide 25: Conversion of multi-level logic to NAND gates
Level 1 Level 2 Level 3 Level 4
original
AND-OR network
A
C
D
B
B
\C
F
introduction and
conservation of bubbles
A
C
D
B
B
\C
F
redrawn in terms
of conventional
NAND gates
A
C
D
\B
B
\C
F
F = A (B + C D) + B C’

## Slide 26: Conversion of multi-level logic to NORs
Level 1 Level 2 Level 3 Level 4
A
C
D
B
B
\C
F
original
AND-OR network
introduction and
conservation of bubbles
A
C
D
B
B
\C
F
redrawn in terms
of conventional
NOR gates
\A
\C
\D
B
\B
C
F
F = A (B + C D) + B C’

## Slide 27: Conversion between forms
Example
A
X
B
C
D
F
original circuit
A
X
B
C
D
F
add double bubbles to invert all inputs of OR gate
\D
A
B
C
F
\D
A
X
B
C
F
\X
insert inverters to eliminate double bubbles on a wire
add double bubbles to invert output of AND gate
X

## Slide 28: AND-OR-invert gates
&
&
+
2x2 AOI gate
symbol
&
&
+
3x2 AOI gate
symbol
NAND NAND
Invert
possible implementation
A
B
C
D
Z
AND
OR Invert
logical concept
A
B
C
D
Z
AOI function: three stages of logic — AND, OR, Invert
  multiple gates "packaged" as a single circuit block

## Slide 29: Conversion to AOI forms
&
&
+
A’
B’
A
B
F
General procedure to place in AOI form
  compute the complement of the function in sum-of-products form
  by grouping the 0s in the Karnaugh map
Example: XOR implementation
  A xor B = A’ B + A B’
  AOI form:
    F = (A’ B’ + A B)’

## Slide 30: Examples of using AOI gates
each implemented in a single 2x2 AOI gate
Example:
  F = A B + A C’ + B C’
  F = (A’ B’ + A’ C + B’ C)’
  Implemented by 2-input 3-stack AOI gate
  F = (A + B) (A + C’) (B + C’)
  F = [(A’ + B’) (A’ + C) (B’ + C)]’
  Implemented by 2-input 3-stack OAI gate
Example: 4-bit equality function
  Z = (A0 B0 + A0’ B0’)(A1 B1 + A1’ B1’)(A2 B2 + A2’ B2’)(A3 B3 + A3’ B3’)

## Slide 31: Examples of using AOI gates (cont’d)
high if A0  B0 low if A0 = B0
if all inputs are low
then Ai = Bi, i=0,...,3
output Z is high
conservation of bubbles
A0
B0
A1
B1
A2
B2
A3
B3
&
&
+
&
&
+
&
&
+
&
&
+
NOR
Z
Example: AOI implementation of 4-bit equality function

## Slide 32: Summary for multi-level logic
Advantages
  circuits may be smaller
  gates have smaller fan-in
  circuits may be faster
Disadvantages
  more difficult to design
  tools for optimization are not as good as for two-level
  analysis is more complex

## Slide 33: Time behavior of combinational networks
Waveforms
  visualization of values carried on signal wires over time
  useful in explaining sequences of events (changes in value)
Simulation tools are used to create these waveforms
  input to the simulator includes gates and their connections
  input stimulus, that is, input signal waveforms
Some terms
  gate delay — time for change at input to cause change at output
    min delay – typical/nominal delay – max delay
    careful designers design for the worst case
  rise time — time for output to transition from low to high voltage
  fall time — time for output to transition from high to low voltage
  pulse width — time that an output stays high or stays low between changes

## Slide 34: Momentary changes in outputs
F is not always 0
pulse 3 gate-delays wide
D remains high for
three gate delays after
A changes from low to high
F
A
B
C
D
Can be useful — pulse shaping circuits
Can be a problem — incorrect circuit operation (glitches/hazards)
Example: pulse shaping circuit
  A’ • A = 0
  delays matter

## Slide 35: Oscillatory behavior
initially undefined
close switch
open switch
+
open switch
resistor
A
B
C
D
Another pulse shaping circuit

## Slide 36: Hardware description languages
Describe hardware at varying levels of abstraction
Structural description
  textual replacement for schematic
  hierarchical composition of modules from primitives
Behavioral/functional description
  describe what module does, not how
  synthesis generates circuit for module
Simulation semantics

## Slide 37: HDLs
Abel (circa 1983) - developed by Data-I/O
  targeted to programmable logic devices
  not good for much more than state machines
ISP (circa 1977) - research project at CMU
  simulation, but no synthesis
Verilog (circa 1985) - developed by Gateway (absorbed by Cadence)
  similar to Pascal and C
  delays is only interaction with simulator
  fairly efficient and easy to write
  IEEE standard
VHDL (circa 1987) - DoD sponsored standard
  similar to Ada (emphasis on re-use and maintainability)
  simulation semantics visible
  very general but verbose
  IEEE standard

## Slide 38: Verilog
Supports structural and behavioral descriptions
Structural
  explicit structure of the circuit
  e.g., each logic gate instantiated and connected to others
Behavioral
  program describes input/output behavior of circuit
  many structural implementations could have same behavior
  e.g., different implementation of one Boolean function
We’ll mostly be using behavioral Verilog in Aldec ActiveHDL
  rely on schematic when we want structural descriptions

## Slide 39: Structural model
module xor_gate (out, a, b); input a, b; output out; wire abar, bbar, t1, t2; inverter invA (abar, a); inverter invB (bbar, b); and_gate and1 (t1, a, bbar); and_gate and2 (t2, b, abar); or_gate or1 (out, t1, t2);
endmodule

## Slide 40: Simple behavioral model
module xor_gate (out, a, b); input a, b; output out;
reg out;
assign #6 out = a ^ b;
endmodule
Continuous assignment
delay from input change to output change
simulation register - keeps track of value of signal

## Slide 41: Simple behavioral model
module xor_gate (out, a, b); input a, b; output out; reg out; always @(a or b) begin
#6 out = a ^ b;
end
endmodule
always block
specifies when block is executed ie. triggered by which signals

## Slide 42: Driving a simulation through a “testbench”
module testbench (x, y); output x, y; reg [1:0] cnt; initial begin cnt = 0; repeat (4) begin #10 cnt = cnt + 1; $display ("@ time=%d, x=%b, y=%b, cnt=%b", $time, x, y, cnt); end #10 $finish; end assign x = cnt[1];
assign y = cnt[0]; endmodule
2-bit vector
initial block executed only once at start of simulation
directive to stop simulation
print to a console

## Slide 43: Complete simulation
Instantiate stimulus component and device to test in a schematic
a
b
z
test-bench
x
y

## Slide 44: Comparator example
module Compare1 (Equal, Alarger, Blarger, A, B); input A, B; output Equal, Alarger, Blarger; assign #5 Equal = (A & B) | (~A & ~B); assign #3 Alarger = (A & ~B); assign #3 Blarger = (~A & B);
endmodule

## Slide 45: More complex behavioral model
module life (n0, n1, n2, n3, n4, n5, n6, n7, self, out); input n0, n1, n2, n3, n4, n5, n6, n7, self; output out; reg out; reg [7:0] neighbors;
reg [3:0] count; reg [3:0] i; assign neighbors = {n7, n6, n5, n4, n3, n2, n1, n0};
always @(neighbors or self) begin count = 0; for (i = 0; i < 8; i = i+1) count = count + neighbors[i]; out = (count == 3); out = out | ((self == 1) & (count == 2)); end
endmodule

## Slide 46: Hardware description languages vs. programming languages
Program structure
  instantiation of multiple components of the same type
  specify interconnections between modules via schematic
  hierarchy of modules (only leaves can be HDL in Aldec ActiveHDL)
Assignment
  continuous assignment (logic always computes)
  propagation delay (computation takes time)
  timing of signals is important (when does computation have its effect)
Data structures
  size explicitly spelled out - no dynamic structures
  no pointers
Parallelism
  hardware is naturally parallel (must support multiple threads)
  assignments can occur in parallel (not just sequentially)

## Slide 47: Hardware description languages and combinational logic
Modules - specification of inputs, outputs, bidirectional, and internal signals
Continuous assignment - a gate’s output is a function of its inputs at all times (doesn’t need to wait to be "called")
Propagation delay- concept of time and delay in input affecting gate output
Composition - connecting modules together with wires
Hierarchy - modules encapsulate functional blocks

## Slide 48: Working with combinational logic summary
Design problems
  filling in truth tables
  incompletely specified functions
  simplifying two-level logic
Realizing two-level logic
  NAND and NOR networks
  networks of Boolean functions and their time behavior
Time behavior
Hardware description languages
Later
  combinational logic technologies
  more design case studies