## Slide 1: Sequential logic implementation
Implementation
  random logic gates and FFs
  programmable logic devices (PAL with FFs)
Design procedure
  state diagrams
  state transition table
  state assignment
  next state functions

## Slide 2: Median filter FSM
Remove single 0s between two 1s (output = NS3)
000
0
1
0
100
010
110
111
011
001
1
1
1
1
1
1
0
0
0
0
0
Reset
I PS1 PS2 PS3 NS1 NS2 NS3 0 0 0 0 0 0 0 0 0 0 1 0 0 0 0 0 1 0 0 0 1 0 0 1 1 0 0 1 0 1 0 0 0 1 0 0 1 0 1 X X X 0 1 1 0 0 1 1 0 1 1 1 0 1 1 1 0 0 0 1 0 0 1 0 0 1 1 0 0 1 0 1 0 1 1 1 1 0 1 1 1 1 1 1 1 0 0 1 1 0 1 1 0 1 X X X 1 1 1 0 1 1 1 1 1 1 1 1 1 1

## Slide 3: Median filter FSM (cont’d)
Realized using the standard procedure and individual FFs and gates
I PS1 PS2 PS3 NS1 NS2 NS3 0 0 0 0 0 0 0 0 0 0 1 0 0 0 0 0 1 0 0 0 1 0 0 1 1 0 0 1 0 1 0 0 0 1 0 0 1 0 1 X X X 0 1 1 0 0 1 1 0 1 1 1 0 1 1 1 0 0 0 1 0 0 1 0 0 1 1 0 0 1 0 1 0 1 1 1 1 0 1 1 1 1 1 1 1 0 0 1 1 0 1 1 0 1 X X X 1 1 1 0 1 1 1 1 1 1 1 1 1 1
NS1 = Reset’ (I)
NS2 = Reset’ ( PS1 + PS2 I )
NS3 = Reset’ PS2
O = PS3

## Slide 4: Median filter FSM (cont’d)
But it looks like a shift register if you look at it right
000
0
1
0
100
010
110
111
011
001
1
1
1
1
1
1
0
0
0
0
0
Reset
000
0
1
0
100
010
110
111
011
001
1
1
1
1
1
1
0
0
0
0
0
Reset
101
1
0

## Slide 5: Median filter FSM (cont’d)
An alternate implementation with S/R FFs
The set input (S) does the median filter function by making the next state 111 whenever the input is 1 and PS2 is 1 (1 input to state x1x)
R = Reset
S = PS2 I
NS1 = I
NS2 = PS1
NS3 = PS2
O = PS3
Out
CLK
D
Q
R
S
D
Q
R
S
D
Q
R
S
In
Reset

## Slide 6: Implementation using PALs
D Q
Q
Programmable logic building block for sequential logic
  macro-cell: FF + logic
    D-FF
    two-level logic capability like PAL (e.g., 8 product terms)

## Slide 7: Vending machine example (Moore PLD mapping)
D0 = reset'(Q0'N + Q0N' + Q1N + Q1D)
D1 = reset'(Q1 + D + Q0N)
OPEN = Q1Q0
D
Q
D
Q
D
Q
Q0
Q1
Open
Com
Seq
Seq
CLK
N
D
Reset

## Slide 8: Vending machine (synch. Mealy PLD mapping)
OPEN = reset'(Q1Q0N' + Q1N + Q1D + Q0'ND + Q0N'D)
OPEN
D
Q
D
Q
D
Q
Q0
Q1
Open
Seq
Seq
Seq
CLK
N
D
Reset

## Slide 9: 22V10 PAL
Combinational logic elements (SoP)
Sequential logic elements (D-FFs)
Up to 10 outputs
Up to 10 FFs
Up to 22 inputs

## Slide 10: 22V10 PAL Macro Cell
Sequential logic element + output/input selection

## Slide 11: Light Game FSM
Tug of War game
  7 LEDs, 2 push buttons (L, R)
LED (3)
LED (2)
LED (1)
LED (0)
LED (6)
LED (5)
LED (4)
RESET
R
R
L
R
L
R
L
R
L
L

## Slide 12: Light Game FSM Verilog
module Light_Game (LEDS, LPB, RPB, CLK, RESET);
input LPB ;
input RPB ;
input CLK ;
input RESET;
output [6:0] LEDS ;
reg [6:0] position;
reg left;
reg right;
always @(posedge CLK)
begin
left <= LPB;
right <= RPB;
if (RESET) position <= 7'b0001000;
else if ((position == 7'b0000001) || (position == 7'b1000000)) ;
else if (L) position <= position << 1;
else if (R) position <= position >> 1;
end
endmodule
wire L, R;
assign L = ~left && LPB;
assign R = ~right && RPB;
assign LEDS = position;
combinational logic
sequential logic

## Slide 13: Example: traffic light controller
A busy highway is intersected by a little used farmroad
Detectors C sense the presence of cars waiting on the farmroad
  with no car on farmroad, light remain green in highway direction
  if vehicle on farmroad, highway lights go from Green to Yellow to Red, allowing the farmroad lights to become green
  these stay green only as long as a farmroad car is detected but never longer than a set interval
  when these are met, farm lights transition from Green to Yellow to Red, allowing highway to return to green
  even if farmroad vehicles are waiting, highway gets at least a set interval as green
Assume you have an interval timer that generates:
  a short time pulse (TS) and
  a long time pulse (TL),
  in response to a set (ST) signal.
  TS is to be used for timing yellow lights and TL for green lights

## Slide 14: Example: traffic light controller (cont’)
highway
farm road
car sensors
Highway/farm road intersection

## Slide 15: Example: traffic light controller (cont’)
Tabulation of inputs and outputs inputs description outputs description reset place FSM in initial state HG, HY, HR assert green/yellow/red highway lights C detect vehicle on the farm road FG, FY, FR assert green/yellow/red highway lights TS short time interval expired ST start timing a short or long interval TL long time interval expired
Tabulation of unique states – some light configurations imply others state description HG highway green (farm road red) HY highway yellow (farm road red) FG farm road green (highway red) FY farm road yellow (highway red)

## Slide 16: Example: traffic light controller (cont’)
State diagram
Reset
TS'
TS / ST
(TL•C)'
TL•C / ST
TS'
TS / ST
(TL+C')'
TL+C' / ST
HG
FG
FY
HY

## Slide 17: Example: traffic light controller (cont’)
Inputs Present State Next State Outputs C TL TS ST H F 0 – – HG HG 0 Green Red – 0 – HG HG 0 Green Red 1 1 – HG HY 1 Green Red – – 0 HY HY 0 Yellow Red – – 1 HY FG 1 Yellow Red 1 0 – FG FG 0 Red Green 0 – – FG FY 1 Red Green – 1 – FG FY 1 Red Green – – 0 FY FY 0 Red Yellow – – 1 FY HG 1 Red Yellow
SA1: HG = 00 HY = 01 FG = 11 FY = 10 SA2: HG = 00 HY = 10 FG = 01 FY = 11 SA3: HG = 0001 HY = 0010 FG = 0100 FY = 1000 (one-hot)
output encoding – similar problem to state assignment (Green = 00, Yellow = 01, Red = 10)
Generate state table with symbolic states
Consider state assignments

## Slide 18: Logic for different state assignments
SA1 NS1 = C•TL'•PS1•PS0 + TS•PS1'•PS0 + TS•PS1•PS0' + C'•PS1•PS0 + TL•PS1•PS0 NS0 = C•TL•PS1'•PS0' + C•TL'•PS1•PS0 + PS1'•PS0 ST = C•TL•PS1'•PS0' + TS•PS1'•PS0 + TS•PS1•PS0' + C'•PS1•PS0 + TL•PS1•PS0 H1 = PS1 H0 = PS1'•PS0 F1 = PS1' F0 = PS1•PS0‘
SA2 NS1 = C•TL•PS1' + TS'•PS1 + C'•PS1'•PS0 NS0 = TS•PS1•PS0' + PS1'•PS0 + TS'•PS1•PS0 ST = C•TL•PS1' + C'•PS1'•PS0 + TS•PS1 H1 = PS0 H0 = PS1•PS0' F1 = PS0' F0 = PS1•PS0
SA3 NS3 = C'•PS2 + TL•PS2 + TS'•PS3 NS2 = TS•PS1 + C•TL'•PS2 NS1 = C•TL•PS0 + TS'•PS1 NS0 = C'•PS0 + TL'•PS0 + TS•PS3 ST = C•TL•PS0 + TS•PS1 + C'•PS2 + TL•PS2 + TS•PS3 H1 = PS3 + PS2 H0 = PS1 F1 = PS1 + PS0 F0 = PS3

## Slide 19: Sequential logic implementation summary
Models for representing sequential circuits
  finite state machines and their state diagrams
  Mealy, Moore, and synchronous Mealy machines
Finite state machine design procedure
  deriving state diagram
  deriving state transition table
  assigning codes to states
  determining next state and output functions
  implementing combinational logic
Implementation technologies
  random logic + FFs
  PAL with FFs (programmable logic devices – PLDs)