## Slide 1
EECS 20
Lecture 38 (April 27, 2001)
Tom Henzinger
Review
Revised by Matteo Zavatteri and Tiziano Villa, Fall 2020

## Slide 2
Transducive System
Input Value
Output Value
transduciveSystem : Values  Values
Reactive System
Input Signal
OutputSignal
reactiveSystem : [ Time  Values ]  [ Time  Values ]

## Slide 3
Discrete time: Time = Nats0 = { 0, 1, 2, … }
Continuous time: Time = Reals+ = { x  Reals | x  0 }

## Slide 4
A reactive system
F : [ Time  Values ]  [ Time  Values ]
is memory-free
iff
there exists a transducive system
f : Values  Values
such that
 x  [ Time  Values ] ,  y  Time,
( F (x) ) (y) = f ( x (y) ) .

## Slide 5
A reactive system
F : [ Time  Values ]  [ Time  Values ]
is causal
iff
 x, y  [ Time  Values ] ,  z  Time,
if (  t  Time, t  z  x (t) = y (t) )
then ( F (x) ) (z) = ( F (y) ) (z) .

## Slide 6
The Delay System
Delayc : [ Time  Values ]  [ Time  Values ]
such that  x  [ Time  Values ] ,  y  Time,
( Delay (x) ) (y) =
c if y < 1
x (y-1) if y  1
{

## Slide 7
Discrete-time delay over finite set of values :
finite memory
Continuous-time delay, or infinite set of values:
infinite memory

## Slide 8
Legal Transducive Block Diagrams
-all components are transducive systems
-no cycles
e.g., combinational circuits
Legal Reactive Block Diagrams
-all components are memory-free or delay systems
-every cycle contains at least one delay
e.g., sequential circuits

## Slide 9
Discrete-time reactive systems with
finite memory
are naturally implemented as
finite state machines.

## Slide 10
A Discrete-Time Reactive System
Nats0  Inputs
Nats0  Outputs
F : [ Nats0  Inputs ]  [ Nats0  Outputs ]
F

## Slide 11
State Machine Implementation
Nats0  Inputs
Nats0  Outputs
DinitialState
Update
1
1
2
2
Nats0 States
Nats0 States
update : States  Inputs  States  Outputs
initialState  States
F
memory-free
delay stores state

## Slide 12
Deterministic State Machine
Inputs ( set of possible input values )
Outputs ( set of possible output values )
States ( set of states )
initialState  States
update : States  Inputs  States  Outputs

## Slide 13
Any block diagram of N state machines with the state spaces
States1, States2, … StatesN
can be implemented by a single state machine with the state space
States1  States2  …  StatesN .
This is called a “product machine”.
Product of State Machines

## Slide 14
Deterministic Reactive System:
for every input signal, there is exactly one output signal.
DetSys : [ Time  Inputs ]  [ Time  Outputs ]
Function:

## Slide 15
Nondeterministic Reactive System:
for every input signal, there is one or more output signals.
NondetSys  [ Time  Inputs ]  [ Time  Outputs ]
such that  x  [ Time  Inputs ],  y  [ Time  Outputs ], (x,y)  NondetSys
Binary relation:
Every pair (x,y)  NondetSys is called a behavior.

## Slide 16
System S1 refines system S2
iff
1. Time [S1] = Time [S2] ,
2. Inputs [S1] = Inputs [S2] ,
3. Outputs [S1] = Outputs [S2] ,
4. Behaviors [S1]  Behaviors [S2] .
S1 is a more detailed description of S2;
S2 is an abstraction or property of S1.

## Slide 17
Systems S1 and S2 are equivalent
iff
1. Time [S1] = Time [S2] ,
2. Inputs [S1] = Inputs [S2] ,
3. Outputs [S1] = Outputs [S2] ,
4. Behaviors [S1] = Behaviors [S2] .

## Slide 18
Nondeterministic State Machine
Inputs
Outputs
States
possibleInitialStates  States
possibleUpdates : States  Inputs  P( States  Outputs ) \ Ø
receptiveness (i.e., machine must be prepared to accept every input)

## Slide 19
State Machines
Deterministic
 
Output-deterministic
 
Nondeterministic
X
X

## Slide 20
A state machine is deterministic
iff
there is only one initial state, and
for every state and every input, there is only one successor state.
A state machine is output-deterministic
iff
there is only one initial state, and
for every state and every input-output pair, there is only one successor state.

## Slide 21
For deterministic M2 :
M1 is simulated by M2 iff M1 is equivalent to M2.
For output-deterministic M2 :
M1 is simulated by M2 iff M1 refines M2.
For nondeterministic M2 :
M1 is simulated by M2 implies M1 refines M2.
condition on infinitely many behaviors
relation between finitely many states

## Slide 22
A binary relation S  States [M1]  States [M2] is a simulation of M1 by M2
iff
1.  p  possibleInitialStates [M1] ,
 q  possibleInitialStates [M2], ( p, q )  S and
2.  p  States [M1] ,  q  States [M2] ,
if ( p, q )  S ,
then  x  Inputs ,  y  Outputs ,  p’  States [M1] ,
if ( p’, y )  possibleUpdates [M1] ( p, x )
then  q’  States [M2] ,
( q’, y )  possibleUpdates [M2] ( q, x ) and
( p’, q’ )  S .

## Slide 23
To check if M1 refines M2, check if M1 is simulated by det(M2):
M1 refines M2
iff
M1 refines det(M2)
iff
M1 is simulated by det(M2).
output-deterministic

## Slide 24
If M2 is an output-deterministic state machine, then a simulation S of M1 by M2 can be found as follows:
1. If p  possibleInitialStates [M1] and
possibleInitialStates [M2] = { q } ,
then (p,q)  S.
2. If (p,q)  S and
(p’,y)  possibleUpdates [M1] (p,x) and
possibleUpdates [M2] (q,x) = { (q’,y) } ,
then (p’,q’)  S.

## Slide 25
Output-Determinization
Given: nondeterministic state machine M
Find: output-deterministic state machine det(M) that is equivalent to M
Inputs [det(M)] = Inputs [M]
Outputs [det(M)] = Outputs [M]

## Slide 26
The Subset Construction
Let initialState [ det(M) ] = possibleInitialStates [M] ;
Let States [ det(M) ] = { initialState [det(M)] } ;
Repeat as long as new transitions can be added to det(M) :
Choose P  States [det(M)] and (x,y)  Inputs  Outputs ;
Let Q = { q  States [M] |  p  P, (q,y)  possibleUpdates [M] (p,x) } ;
If Q  Ø then
Let States [det(M)] = States [det(M)]  {Q} ;
Let update [det(M)] (P,x) = (Q,y) .

## Slide 27
Minimization Algorithm
Input : nondeterministic state machine M
Output : minimize (M), the state machine with the fewest states that is bisimilar to M
(the result is unique up to renaming of states)

## Slide 28
A binary relation B  States [M1]  States [M2] is a bisimulation between M1 and M2
iff
A1.  p  possibleInitialStates [M1] ,
 q  possibleInitialStates [M2], ( p, q )  B, and
A2.  p  States [M1] ,  q  States [M2] ,
if ( p, q )  B ,
then  x  Inputs ,  y  Outputs ,  p’  States [M1] ,
if ( p’, y )  possibleUpdates [M1] ( p, x )
then  q’  States [M2] ,
( q’, y )  possibleUpdates [M2] ( q, x ) and
( p’, q’ )  B , and

## Slide 29
B1.  q  possibleInitialStates [M2] ,
 p  possibleInitialStates [M1], ( p, q )  B, and
B2.  p  States [M1] ,  q  States [M2] ,
if ( p, q )  B ,
then  x  Inputs ,  y  Outputs ,  q’  States [M2] ,
if ( q’, y )  possibleUpdates [M2] ( q, x )
then  p’  States [M1] ,
( p’, y )  possibleUpdates [M1] ( p, x ) and
( p’, q’ )  B .
and

## Slide 30
For nondeterministic state machines M1 and M2,
M1 is equivalent to M2

M1 simulates M2 and M2 simulates M1
 
M1 and M2 are bisimilar.
X
For output-deterministic state machines M1 and M2,
M1 is equivalent to M2

M1 and M2 are bisimilar.
X

## Slide 31
1. Let Q be set of all reachable states of M.
2. Maintain a set P of state sets:
Initially let P = { Q }.
Repeat until no longer possible: split P.
3. When done, every state set in P represents a single state of the smallest state machine bisimilar to M.
Minimization Algorithm

## Slide 32
Split P
If there exist
two state sets R  P and R’  P
two states r1  R and r2  R
an input x  Inputs
an output y  Outputs
such that
 r’  R’, ( r’, y )  possibleUpdates ( r1, x ) and
 r’  R’, ( r’, y )  possibleUpdates ( r2, x )
then
let R1 = { r  R |  r’  R’, ( r’, y )  possibleUpdates ( r, x ) } ;
let R2 = R \ R1 ;
let P = ( P \ { R } )  { R1, R2 } .

## Slide 33
The Finite-State Safety Control Problem
Given
finite-state machine Plant
1.
2. set Error of states of Plant
Find
finite-state machine Controller
such that the composite system never enters a state in Error

## Slide 34
The Finite-State Progress Control Problem
Given
finite-state machine Plant
1.
2. set Target of states of Plant
Find
finite-state machine Controller
such that the composite system is guaranteed to enter a state in Target

## Slide 35
Compute the safety-uncontrollable states of Plant
Every state in Error is safety-uncontrollable.
For all states s,
if for all inputs i there exist a safety-uncontrollable state s’ and an output o such that (s’,o)  possibleUpdates (s,i)
then s is safety-uncontrollable.

## Slide 36
Compute the progress-controllable states of Plant
Every state in Target is progress-controllable.
For all states s,
if there exists an input i for all states s’ and outputs o if (s’,o)  possibleUpdates (s,i) then s’ is progress-controllable
then s is progress-controllable.

## Slide 37
Typical Exam Questions
A. Convert between the following system representations:
  1. Mathematical input-output definition 2. Transition diagram 3. Block diagram
Apply the following algorithms on state machines:
  1. Product construction 2. Subset construction 3. Check for existence of a simulation 4. Minimization 5. Compute controllable states
Explain the following concepts:
    1. Memory-free vs. finite-state vs. infinite-state 2. Equivalence/refinement vs. simulation vs. bisimulation 3. Safety vs. progress control