## Slide 1
EECS 20
Lecture 5 (January 26, 2001)
Tom Henzinger
Signals

## Slide 2
Quiz
 set x, x  P(x)
false
 function f, { x  domain (f) | x = f(x) }
not well-formed
 n  Nats, n = 2  ( n, n+1 )  { 1, 2, 3 } 2
true
 f  [Nats  Nats], f(x) = x 2
free x

## Slide 3
1 Systems are functions
2 Signals are functions

## Slide 4
Audio Signals
sound : ContinuousTime  AirPressure
Reals+
Reals+
Let ContinuousTime = Reals+ = { x  Reals | x  0 } .
Let AirPressure = Reals+ .

## Slide 5
normalizedSound : ContinuousTime  NormalizedPressure
Reals+
Reals
Let NormalizedPressure = Reals .

## Slide 6
normalizedSound : ContinuousTime  NormalizedPressure
such that  x  ContinuousTime,
normalizedSound (x) = sound (x) – ambientAirPressure .
Reals+
Reals
Let NormalizedPressure = Reals .

## Slide 7
sampledSound : DiscreteTime  NormalizedPressure
samplingPeriod (sec) = 1 / samplingFrequency (Hz)
Nats0
Reals
Let DiscreteTime = Nats0 .

## Slide 8
Nats0
Reals
Let DiscreteTime = Nats0 .
sampledSound : DiscreteTime  NormalizedPressure
such that  x  DiscreteTime,
sampledSound (x) = normalizedSound ( samplingPeriod · x ) .

## Slide 9
quantizedSound : DiscreteTime  ComputerInts
maxint = 2 wordsize - 1
Nats0
ComputerInts
Let ComputerInts = { x  Ints | -maxint  x  maxint } .

## Slide 10
quantizedSound : DiscreteTime  ComputerInts
such that  x  DiscreteTime,
quantizedSound (x) = trunc (  sampledSound (x)  , maxint ) .
Nats0
ComputerInts
Let ComputerInts = { x  Ints | -maxint  x  maxint } .

## Slide 11
 : Reals  Ints
such that  x  Reals,  x  = max { y  Ints | y  x } .
trunc : Ints  ComputerInts  ComputerInts
such that  x  Ints,  y  ComputerInts,
x if -y  x  y
trunc (x,y) = y if x > y
-y if x < -y .


## Slide 12
 x  Reals,  y  Reals,
let max x = y  y  x   ( z  x, z  y ) .
x  Ints,  y  ComputerInts,
( -y  x  y  trunc (x,y) = x ) 
( x > y  trunc (x,y) = y ) 
( x < -y  trunc (x,y) = -y ) .

## Slide 13
sound : Reals+  Reals analog signal
quantizedSound : Nats0  Ints digital signal

## Slide 14
Video Signals
movie : DiscreteTime  Frames
AnalogFrames = [ DiscreteVerticalSpace  HorizontalSpace  Intensity ]
DigitalFrames = [ DiscreteVerticalSpace  DiscreteHorizontalSpace  DiscreteIntensity ]
( typical frequency = 30 Hz )

## Slide 15
Sheet of paper : VerticalSpace = [ 0, 11 ]
HorizontalSpace = [ 0, 8.5 ]
TV : DiscreteVerticalSpace = { 1, 2, … , 525 }
DiscreteIntensity = ComputerInts
ColorIntensity = Intensity3
LCD : DiscreteVerticalSpace = { 1, 2, … , 1024 }
DiscreteHorizontalSpace = { 1, 2, … , 1280 }

## Slide 16
Currying
Frames =
[ VerticalSpace  HorizontalSpace  Intensity ] =
[ VerticalSpace  [ HorizontalSpace  Intensity ] ]
For all sets A, B, C,
[ A  B  C ] = [ A  [ B  C ] ] .

## Slide 17
Currying
movie 
[ DiscreteTime  [ VSpace  [ HSpace  Intensity ]]] =
[ DiscreteTime  VSpace  HSpace  Intensity ]
For all sets A, B, C,
[ A  B  C ] = [ A  [ B  C ] ] .

## Slide 18
More Signals
position : Time  Space
ContinuousTime = Reals+ . DiscreteTime = Nats0 . DiscTwoSpace = Ints2 . ContThreeSpace = Reals3 .

## Slide 19
More Signals
position : Time  Space
velocity : Time  DerivativeSpace
DerivativeSpace = Space .
ContinuousTime = Reals+ . DiscreteTime = Nats0 . DiscTwoSpace = Ints2 . ContThreeSpace = Reals3 .

## Slide 20
More Signals
position : Time  Space
velocity : Time  DerivativeSpace
positionVelocity: Time  Space  DerivativeSpace
such that  x  Time, positionVelocity (x) = ( position (x) , velocity (x) ) .
DerivativeSpace = Space .
ContinuousTime = Reals+ . DiscreteTime = Nats0 . DiscTwoSpace = Ints2 . ContThreeSpace = Reals3 .